## Slide 1: RDMA in Data Centers
SIGCOMM
With slides from Chuanxiong Guo et al.

## Slide 2
The Rising of Cloud Computing
40
AZURE REGIONS

## Slide 3: Data Centers

## Slide 4
Data Centers

## Slide 5: Data center networks (DCN)
Cloud scale services: IaaS, PaaS, Search, BigData, Storage, Machine Learning, Deep Learning
Services are latency sensitive or bandwidth hungry or both
Cloud scale services need cloud scale computing and communication infrastructure

## Slide 6: Data center networks (DCN)
Single ownership
Large scale
High bisection bandwidth
Commodity Ethernet switches
TCP/IP protocol suite
Spine
Leaf
ToR
Podset
Pod
Servers

## Slide 7: But TCP/IP is not doing well

## Slide 8: TCP latency
405us (P50)
716us (P90)
2132us (P99)
Long latency tail
Pingmesh measurement results

## Slide 9: TCP processing overhead (40G)
Sender
Receiver
8 tcp connections
40G NIC

## Slide 10: An RDMA renaissance story

## Slide 11: RDMA
Remote Direct Memory Access (RDMA): Method of accessing memory on a remote system without interrupting the processing of the CPU(s) of that system
RDMA offloads packet processing protocols to the NIC
RDMA features:
  Remote
    data transfers between nodes in a network
  Direct
    no Operating System Kernel involvement in transfers
    everything about a transfer offloaded onto Interface Card
  Memory
    transfers between user space application virtual memory
    no extra copying or buffering
  Access
    send, receive, read, write, atomic operations

## Slide 12: RDMA Evolutions
InfiniBand – (41.8% of top 500 supercomputers) (1997)
  SDR 4x – 8 Gbps
  DDR 4x – 16 Gbps
  QDR 4x – 32 Gbps
  FDR 4x – 54 Gbps
iWarp – Internet Wide Area RDMA Protocol (2010)
  10 Gbps
RoCE – RDMA over Converged Ethernet (2014)
  10 Gbps
  40 Gbps

## Slide 13: RDMA Illustration

## Slide 14: RDMA Layering
User Application
OFA Verbs API
Physical
Data Link
Network
Transport
IWARP “RNIC”
RoCE “NIC”
InfiniBand “HCA”
RDMAP
DDP
MPA
TCP
IP
IB Transport API
IB Transport
IB Network
Ethernet MAC & LLC
IB Link
Ethernet PHY
IB PHY
OSI
Layers

## Slide 15: Software RDMA Drivers
Softiwarp
  www.zurich.ibm.com/sys/rdma
  open source kernel module that implements iWARP protocols on top of ordinary kernel TCP sockets
  interoperates with hardware iWARP at other end of wire
Soft RoCE
  www.systemfabricworks.com/downloads/roce
  open source IB transport and network layers in software over ordinary Ethernet
  interoperates with hardware RoCE at other end of wire

## Slide 16: Comparisons between TCP and RDMA
Common features:
Both utilize the client-server model
Both require a connection for reliable transport
Both provide a reliable transport mode
  TCP provides a reliable in-order sequence of bytes
  RDMA provides a reliable in-order sequence of messages
Differences:
“zero copy” – data transferred directly from virtual memory on one node to virtual memory on another node
“kernel bypass” – no operating system involvement during data transfers
asynchronous operation – threads not blocked during I/O transfers

## Slide 17: TCP/IP Setup
User
App
Kernel
Stack
CA
Wire
client
server
setup
setup
connect
listen
accept
bind
User
App
Kernel
Stack
CA
Wire
blue lines: control information
red lines: user data
green lines: control and data

## Slide 18: RDMA Setup
User
App
Kernel
Stack
CA
Wire
client
server
setup
setup
rdma_
connect
rdma_listen
rdma_accept
rdma_bind
User
App
Kernel
Stack
CA
Wire
blue lines: control information
red lines: user data
green lines: control and data

## Slide 19: TCP/IP Data Transfer
User
App
Kernel
Stack
CA
Wire
client
server
setup
setup
connect
listen
accept
bind
User
App
Kernel
Stack
CA
Wire
blue lines: control information
data
send
data
recv
red lines: user data
green lines: control and data
transfer
transfer
data
copy
data
copy

## Slide 20: RDMA Data Transfer
User
App
Kernel
Stack
CA
Wire
client
server
setup
setup
rdma_
connect
rdma_listen
rdma_accept
rdma_bind
User
App
Kernel
Stack
CA
Wire
blue lines: control information
data
rdma_
post_
send
data
rdma_
post_
recv
red lines: user data
green lines: control and data
transfer
transfer

## Slide 21: RoCEv2: RDMA over Commodity Ethernet
RoCEv2 for Ethernet based data centers
RoCEv2 encapsulates packets in UDP
OS kernel is not in data path
NIC for network protocol processing and message DMA
TCP/IP
NIC driver
User
Kernel
Hardware
RDMA transport
IP
Ethernet
RDMA app
DMA
RDMA verbs
TCP/IP
NIC driver
Ethernet
RDMA app
DMA
RDMA verbs
Lossless network
RDMA transport
IP

## Slide 22: RDMA benefit: latency reduction
Msg size | TCP P50 (us) | TCP P99 (us) | RDMA P50 (us) | RDMA P99 (us)
1KB | 236 | 467 | 24 | 40
16KB | 580 | 788 | 51 | 117
128KB | 1483 | 2491 | 247 | 551
1MB | 5290 | 6195 | 1783 | 2214
For small msgs (<32KB), OS processing latency matters
For large msgs (100KB+), speed matters

## Slide 23: RDMA benefit: CPU overhead reduction
Sender
Receiver
One ND connection
40G NIC
37Gb/s goodput

## Slide 24: RDMA benefit: CPU overhead reduction
RDMA: Single QP, 88 Gb/s, 1.7% CPU
TCP: Eight connections, 30-50Gb/s,
Client: 2.6%, Server: 4.3% CPU
Intel(R) Xeon(R) CPU E5-2690 v4 @ 2.60GHz, two sockets 28 cores

## Slide 25: RoCEv2 needs a lossless Ethernet network
PFC for hop-by-hop flow control
DCQCN for connection-level congestion control

## Slide 26: Priority-based flow control (PFC)
Hop-by-hop flow control, with eight priorities for HOL blocking mitigation
The priority in data packets is carried in the VLAN tag or DSCP
PFC pause frame: inform the upstream to stop
PFC pause frame
p1
Egress port
Ingress port
p0
p1
p7
Data packet
p0
p0
p1
p7
XOFF threshold
Data packet
PFC pause frame

## Slide 27: DCQCN
CP: Switches use ECN for packet marking
NP: periodically check if ECN-marked packets arrived, if so, notify the sender
RP: adjust sending rate based on NP feedbacks
Sender NIC
Reaction Point
(RP)
Switch
Congestion Point (CP)
Receiver NIC
Notification Point (NP)
DCQCN = Keep PFC + Use ECN + hardware rate-based congestion control

## Slide 28: The lossless requirement poses safety and performance challenges
RDMA transport livelock
PFC deadlock
PFC pause frame storm
Slow-receiver symptom

## Slide 29: RDMA transport livelock
RDMA Send 0
RDMA Send 1
RDMA Send N+1
NAK N
RDMA Send 0
RDMA Send 1
RDMA Send 2
RDMA Send N+2
Go-back-0
Go-back-N
RDMA Send 0
RDMA Send 1
RDMA Send N+1
NAK N
RDMA Send N
RDMA Send N+1
RDMA Send N+2
RDMA Send N+2
Sender
Receiver
Switch
Pkt drop rate 1/256
Sender
Receiver
Receiver
Sender

## Slide 30: PFC deadlock
Our data centers use Clos network
Packets first travel up then go down
No cyclic buffer dependency for up-down routing -> no deadlock
But we did experience deadlock!
Spine
Leaf
ToR
Podset
Pod
Servers

## Slide 31: PFC deadlock
Two tables
  ARP table: IP address to MAC address mapping
  MAC table: MAC address to port mapping
Timeout values for table entries in the two tables are different
  ARP Table: 4 hours
  MAC table: 5 minutes
Consequence
  Incomplete (i.e., missing) MAC table entries for some ports
  If an MAC table entry is missing, packets are flooded to all ports
IP | MAC | TTL
IP0 | MAC0 | 2h
IP1 | MAC1 | 1h
MAC | Port | TTL
MAC0 | Port0 | 5min
MAC1 | - | -
Input
Output
Dst: IP1
ARP table
MAC table

## Slide 32: PFC deadlock
La
Lb
T0
T1
S1
S2
S3
S4
Server
p0
p1
p2
p3
p0
p1
p3
p4
p0
p1
p0
p1
Egress
port
Ingress
port
1
4
3
2
PFC pause frames
p2
S5
Packet drop
Congested port
Dead server
PFC pause frames
Path: {S1, T0, La, T1, S3}
Path: {S1, T0, La, T1, S5}
Path: {S4, T1, Lb, T0, S2}

## Slide 33: PFC deadlock
Root cause: the interaction between the PFC flow control and the Ethernet packet flooding (due to missing MAC forwarding table entry)
  Lead to cyclic buffer dependency
Solution: drop those lossless packets if the ARP table entry is incomplete
Recommendation: do not flood or multicast for lossless traffic

## Slide 34: NIC PFC pause frame storm
A malfunctioning NIC may block the whole network
PFC pause frame storms caused several incidents
Solution: watchdogs at both NIC and switch sides to stop the storm
  Drop lossless packets
  Stop pause frames
ToRs
Leaf layer
Spine layer
servers
0
1
2
3
4
5
6
7
Malfunctioning NIC
Podset 0
Podset 1

## Slide 35: The slow-receiver symptom
ToR to NIC is 40Gb/s, NIC to server is 64Gb/s
But NICs may generate large number of PFC pause frames
Root cause: NIC is resource constrained
Mitigation
  Large page size for the MTT (memory translation table) entry
  Dynamic buffer sharing at the ToR switch
CPU
DRAM
ToR
QSFP
40Gb/s
PCIe
Gen3 8x8 64Gb/s
MTT
WQEs
QPC
NIC
Server
Pause frames

## Slide 36: Deployment experiences and lessons learned

## Slide 37: Latency reduction
RoCEv2 deployed in Bing world-wide for two and half years
Significant latency reduction
Incast problem solved as no packet drops

## Slide 38: RDMA throughput
Using two podsets each with 500+ servers
5Tb/s capacity between the two podsets
Achieved 3Tb/s inter-podset throughput
Bottlenecked by ECMP routing
Close to 0 CPU overhead

## Slide 39: Latency and throughput tradeoff
L0
T0
L1
T1
L1
L1
S0,0
S0,23
S1,0
S1,23
RDMA latencies increase as data shuffling started
Low latency vs high throughput
us
Before data shuffling
During data shuffling

## Slide 40: Lessons learned
Providing lossless is hard!
Deadlock, livelock, PFC pause frames propagation and storm did happen
Be prepared for the unexpected
  Configuration management, latency/availability, PFC pause frame, RDMA traffic monitoring
NICs are the key to making RoCEv2 work

## Slide 41: Future for RDMA?

## Slide 42
Applications
Technologies
Architectures
Protocols
RDMA for X (Search, Storage, DNN, etc.)
Lossy vs lossless network
Practical, large-scale deadlock free network
RDMA programming
RDMA for heterogenous computing systems
RDMA virtualization
Reducing colleterial damage
RDMA security
Software vs hardware
Inter-DC RDMA

## Slide 43: Will software win?
Historically, software-based packet processing won (multiple times)
  TCP processing overhead analysis by David Clark, et al.
  Non of the stateful TCP offloading took off (e.g., TCP Chimney)
The story is different this time
  Moore’s law is ending
  Accelerators are coming
  Network speed keeps increasing
  Demands for ultra low latency are real

## Slide 44: Is lossless mandatory for RDMA?
There is no binding between RDMA and lossless network
But implementing more sophisticated transport protocol in hardware is a challenge

## Slide 45: RDMA virtualization for the container networking
A router acts as a proxy for the containers
Shared memory for improved performance
Zero copy possible

## Slide 46: RDMA for DNN
TCP does not work for distributed DNN training
For 16-GPU, 2-host speech training with CNTK, TCP communications dominant the training time (72%), RDMA is much faster (44%)

## Slide 47: RDMA Programming
How many LOC for a “hello world” communication using RDMA?
For TCP, it is 60 LOC for client or server code
For RDMA, it is complicated …
  IBVerbs: 600 LOC
  RCMA CM: 300 LOC
  Rsocket: 60 LOC

## Slide 48: RDMA Programming
Make RDMA programming more accessible
  Easy-to-setup RDMA server and switch configurations
  Can I run and debug my RDMA code on my desktop/laptop?
  High quality code samples
Loosely coupled vs tightly coupled (Send/Recv vs Write/Read)

## Slide 49: Summary: RDMA for data centers
RDMA is experiencing a renaissance in data centers
  RoCEv2 has been running safely in Microsoft data centers for two and half years
Many opportunities and interesting problems for high-speed, low-latency RDMA networking
Many opportunities in making RDMA accessible to more developers