## Slide 1: Switch-Centric Data Center Network Architecture

## Slide 2: Outline
Data center network basics
Switch-centric design approach to scalable data center networking
  Fat-tree
  Portland

## Slide 3: What is a Data Center Network?
Network infrastructure that inter-connects a large number of commodity servers
  Each server has an Ethernet interface: 1~10Gbps
  Two types of data communications
    External communications to Internet hosts
      How each client user requests/receives services: gmail, google service, online shopping, …
    Internal communications among servers
      Used for internal data storage, processing and transfer by cloud computing software
Network that serves both “commodity servers” and user clients
  Network functions: routing & forwarding data

## Slide 4: Desired Properties of Solutions
Scaling
  100s to 100,000s of servers
High speed
  1~100s Gbps for server-to-server communications
  No changes in apps; Support of Layer 2 (Ethernet)
Cost effective
  Low power consumption & heat emission
  Cheap infrastructure
Fault tolerance
  Robust against component failures

## Slide 5: Initial Design of DCN (CISCO)

## Slide 6: Scale to Large Server Population: Scale Up

## Slide 7: Scaling and Routing
Scale up
  Add more layers in the hierarchy to scale to larger # of servers
    Starting from 2~3-layer hierarchy
    Similar to the Internet DNS system
Spanning tree based forwarding
  Build a tree for data forwarding (running Internet layer-2 spanning tree protocol)
    Root: core switches
    Servers as leaf of the tree
  Single path between any two servers
    No forwarding loops

## Slide 8: Problem With common DC topology
Expensive hardware cost
  Core switches, aggregation switches
Fault tolerance
  Tree like topology offers a single physical path for each pair of servers
  Single point of failure
Reduced speed for server-to-server communication
  Over subscription of links higher up in the topology
  Trade off between cost and provisioning

## Slide 9: Cost of maintaining switches
Notes: Netgear ~ 3K
Procurve – 4.5K

## Slide 10: Need for Layer-2 In DC
Certain monitoring apps require server with same role to be on the same VLAN
Using same IP on dual homed servers
Allowing growth of server farms.

## Slide 11: Forwarding & Routing: Review of Layer 2 & Layer 3
Layer 2
  One spanning tree for entire network
    Prevents looping
    Ignores alternate paths
Layer 3
  Internet routing design
  Shortest path routing between source and destination
  Best-effort delivery
Notes: In this talk, I shall next explain the problems with current middlebox deployment mechanisms.
I shall then describe how our solution, the policy-aware switching layer simplifies middlebox deployment and achieves the properties I mentioned earlier.
I shall briefly discuss related work, and our prototype implementation and evaluation of the policy-aware switching layer.

## Slide 12: Switch-centric Solution
Switch-centric solution scheme
  Innovations are at the switch that interconnects servers
    Modifying the switch design and operations
  Servers remain unchanged
How to scale? Scale out
  Expand horizontally to scale to large # of servers
  Do not increase depths in the hierarchy
Examples:
  Fat tree
  Portland

## Slide 13: FAT Tree based Solution
An example of switch-centric design
  Servers remain unchanged
Connect servers using a Fat-Tree topology
  Infrastructure consist of cheap devices
    Layer-2 switch is comparably cheaper than Layer-3 routers
    Each port supports same speed as servers
  All devices can transmit at line speed if packets are properly distributed along existing paths

## Slide 14: Fat-Tree Topology

## Slide 15: Problems with a vanilla Fat-tree
Layer-3 routing will only use one of the existing equal-cost paths
Packet re-ordering occurs if layer 3 blindly takes advantage of path diversity
  Packets from the same data session may traverse different paths (with different core/aggregation switches)

## Slide 16: FAT-tree Modified
Enforce special addressing scheme
  Allows servers attached to the same switch to route only through the switch
  Allows intra-pod traffic to stay within pod
  10 (unused).PodNumber.switchnumber.Endserver
Use two-level look-ups to distribute traffic and maintain packet ordering.

## Slide 17: 2 Level Look-ups
First level is prefix lookup
  Used to route down the topology to servers
  Highest 3 bytes (prefix /24)
Second level is a suffix lookup
  Lowest 1 byes (suffix /8)
  Used to route up towards core
  Diffuses and spreads out traffic
  Maintains packet ordering by using the same ports for the same end servers

## Slide 18: Summary
Scaling is a main challenge for data center networking
  Traditional design cannot scale while ensuring fault tolerance, load balancing
New design approach: scale out rather than scale up
FatTree: switch-based scale-out solution

## Slide 19: PortLand (Sigcomm’09)
Core idea: adapt Layer-3 solutions (addressing and routing) to Layer-2
PortLand is a single logical layer-2 data center network fabric that scales to millions of endpoints
PortLand internally separates host identity from host location
  Note IP address plays the dual roles of host ID (for TCP connection) and host location (for routing)
  Uses IP address as host identifier
  Introduces “Pseudo MAC” (PMAC) addresses internally to encode endpoint location
PortLand runs on commodity switch hardware with unmodified hosts/servers

## Slide 20: Goals For Data Center Network Fabrics
Easy configuration and management – Plug and play
Fault tolerance, routing and addressing – Scalability
Commodity switch hardware – Small switch state
Virtualization support – Seamless VM migration

## Slide 21: Layer 2 versus Layer 3 Data Center Fabrics
Technique
Plug and play
Scalability
Small Switch State
Seamless VM
Migration
Layer 2:
Flat MAC Addresses
Layer 3:
IP Addresses
+
+ -
-
-
+
+
-

## Slide 22: Layer 2 versus Layer 3 Data Center Fabrics
Technique
Plug and play
Scalability
Small Switch State
Seamless VM
Migration
Layer 2:
Flat MAC
Addresses
Layer 3:
IP address
Flooding
Host MAC Address
Out Port
9a:57:10:ab:6e 1
62:25:11:bd:2d 3
ff:30:2a:c9:f3 0
…. …
Host IP Address
Out Port
+ -
+
-
+
- -
No change
to IP
endpoint
+
LSR – IP endpoint
Addresses Broadcast 10.2.x.x 0 can change
based 10.4.x.x 1
Location-based addresses mandate manual configuration

## Slide 23: Cost Consideration: Flat Address vs. Location-based Address
Commodity switches today have ~640 KB of low latency, power hungry, expensive on chip memory
– Stores 32 – 64 K flow entries
Assume 10 million virtual endpoints in 500,000 servers in data center
Flat addresses: 10 million address mappings; ~100 MB on chip memory; ~150 times the memory size that can be put on chip today
Location based addresses: 100 – 1000 address mappings; ~10 KB of memory; easily accommodated in switches today

## Slide 24: PortLand: Plug and Play + Small Switch State
10 million virtual endpoints in 500,000 servers in data center
PMAC Address
Out Port
0:2:x:x:x:x 0
0:4:x:x:x:x 1 •100 – 1000 address mappings
0:6:x:x:x:x 2 ~10 KB of memory € easily
0:8:x:x:x:x 3 accommodated in switches today
9
Pair-wise communication
Auto Configuration
+
PortLand switches learn location in topology using pair-wise communication
They assign topologically meaningful addresses to hosts using their location

## Slide 25: PortLand: Main Assumption Hierarchical structure of data center networks: They are multi-level, multi-rooted trees
Cisco Recommended Configuration
Fat Tree

## Slide 26: PortLand: Scalability Challenges
Challenge
State Of Art
Address Resolution
Routing
Forwarding
Broadc Xast based
Broadc Xast based Large s Xwitch state

## Slide 27: Data Center Network
Servers
Switches
Edge
Core
Aggregation

## Slide 28: Imposing Hierarchy On A Multi-Rooted Tree
Pod Number
POD 0 POD 1 POD 2
POD 3

## Slide 29: Imposing Hierarchy On A Multi-Rooted Tree
Position Number
0 1
0
1
0 1
0 1

## Slide 30: Imposing Hierarchy On A Multi-Rooted Tree
0 1
0
1
0 1
0 1
PMAC: pod.position.port.vmid

## Slide 31: Imposing Hierarchy On A Multi-Rooted Tree
PMAC: pod.position.port.vmid
0 1
0
1
0 1
0 1

## Slide 32: Imposing Hierarchy On A Multi-Rooted Tree
PMAC: pod.position.port.vmid
0 1
0
1
0 1
0 1

## Slide 33: Imposing Hierarchy On A Multi-Rooted Tree
0 1
0
1
0 1
0 1
00:00:00:02:00:01
00:00:00:03:00:01
00:00:01:02:00:01
00:00:01:03:00:01
00:01:00:02:00:01
00:01:00:03:00:01
00:01:01:02:00:01
00:01:01:03:00:01
00:02:00:02:00:01
00:02:00:03:00:01
00:02:01:02:00:01
00:02:01:03:00:01
00:03:00:02:00:01
00:03:00:03:00:01
00:03:01:02:00:01
00:03:01:03:00:01

## Slide 34: PortLand: Location Discovery Protocol
Location Discovery Messages (LDMs) exchanged between neighboring switches
Switches self-discover location on boot up
Location characteristic Technique
  Tree level / Role Based on neighbor identity
2) Pod number
Aggregation and edge switches agree on pod number
3) Position number
Aggregation switches help edge switches choose unique position number

## Slide 35: PortLand: Location Discovery Protocol
A0:B1:FD:56:32:01 ?? ?? ??
Switch Identifier
Pod Number
Position
Tree Level

## Slide 36: PortLand: Location Discovery Protocol
A0:B1:FD:56:32:01 ?? ?? ??
Switch Identifier
Pod Number
Position
Tree Level

## Slide 37: PortLand: Location Discovery Protocol
Switch Identifier
Pod Number
Position
Tree Level
A0:B1:FD:56:32:01 ?? ?? ??
0

## Slide 38: PortLand: Location Discovery Protocol
B0:A1:FD:57:32:01 ?? ?? ??
Switch Identifier
Pod Number
Position
Tree Level

## Slide 39: PortLand: Location Discovery Protocol
??
B0:A1:FD:57:32:01 ?? ?? 1
Switch Identifier
Pod Number
Position
Tree Level

## Slide 40: PortLand: Location Discovery Protocol
??
B0:A1:FD:57:32:01 ?? ?? 1
Switch Identifier
Pod Number
Position
Tree Level

## Slide 41: PortLand: Location Discovery Protocol
A0:B1:FD:56:32:01 ?? ?? 0
Propose 1
Switch Identifier
Pod Number
Position
Tree Level

## Slide 42: PortLand: Location Discovery Protocol
D0:B1:AD:56:32:01 ?? ?? 0
Propose 0
Switch Identifier
Pod Number
Position
Tree Level

## Slide 43: PortLand: Location Discovery Protocol
??
A0:B1:FD:56:32:01 ?? 1 0
Yes
Switch Identifier
Pod Number
Position
Tree Level

## Slide 44: PortLand: Location Discovery Protocol
D0:B1:AD:56:32:01 ?? 0 0
Fabric Manager
Switch Identifier
Pod Number
Position
Tree Level

## Slide 45: PortLand: Location Discovery Protocol
D0:B1:AD:56:32:01 ?? 0 0
0
Fabric Manager
Switch Identifier
Pod Number
Position
Tree Level

## Slide 46: PortLand: Location Discovery Protocol
Switch Identifier
Pod Number
Position
Tree Level
??
D0:B1:AD:56:32:01 0 0 0
0
Pod 0
Fabric Manager

## Slide 47: PortLand: Name Resolution
Intercept all ARP packets

## Slide 48: PortLand: Name Resolution
Actual MAC
Pseudo MAC
00:19:B9:FA:88:E2
00:00:01:02:00:01
Assign new end hosts with PMACs

## Slide 49: PortLand: Name Resolution
Actual MAC
Pseudo MAC
00:19:B9:FA:88:E2
00:00:01:02:00:01
Rewrite MAC for packets entering and exiting network

## Slide 50: PortLand: Name Resolution
Actual MAC
Pseudo MAC
00:19:B9:FA:88:E2
00:00:01:02:00:01
Fabric Manager

## Slide 51: PortLand: Fabric Manager
IP Pseudo MAC
10.5.1.2 00:00:01:02:00:01
10.2.4.5 00:02:00:02:00:01
Soft state
Administrator configuration
Fabric Manager
ARP mappings
Network map

## Slide 52: PortLand: Name Resolution
Fabric Manager
10.5.1.2
MAC ??

## Slide 53: PortLand: Name Resolution
Fabric Manager
10.5.1.2
00:00:01:02:00:01

## Slide 54: PortLand: Name Resolution
Address | HWtype | HWAddress | Flags | Mask | Iface
10.5.1.2 | ether | 00:00:01:02:00:01 | C | eth1 | 
ARP replies contain only PMAC

## Slide 55: Portland Prototype
20 OpenFlow NetFPGA switches
TCAM + SRAM for flow entries
Software MAC rewriting
3 tiered fat-tree
16 end hosts

## Slide 56: PortLand: Evaluation
Measurements
Configuration
Results
Network convergence time
65 ms
Keepalive frequency = 10 ms
Fault detection time = 50
ms
RTOmin = 200ms
~200 ms 110ms
RTOmin = 200ms
~200 ms – 600 ms
400 Mbps
TCP convergence time
Multicast convergence time
TCP convergence with VM migration
Control traffic to fabric manager
CPU requirements of fabric manager
27,000+ hosts,
100 ARPs / sec per host
27,000+ hosts,
100 ARPs / sec per host
70 CPU cores

## Slide 57: Recap on PortLand
PortLand is a single logical layer 2 data center network fabric that scales to millions of endpoints
Modify network fabric to
  Work with arbitrary operating systems and virtual machine monitors
  Maintain the boundary between network and end-host administration
Scale Layer 2 via network modifications
  Unmodified switch hardware and end hosts

## Slide 58: Summary
New way to scale out in data center networking design
Switch-centric solution approach
  Keep the servers intact
  Modify the switches
Migrate the Layer-3 (IP) solution ideas to Layer 2
  Addressing (PMAC): encoding location info
    Not flat addressing any more
  Forwarding (using IP routing)?